## Slide 1: RT Logic Hitless Merge Project Luke Josten, Joel Vastbinder, Andrew Blomenberg, and Joey Ferguson
Introduction
Kratos RT Logic partnered with Taylor University and prepared a data merging project for a team of four students to work on. The purpose of the project is to develop effective algorithms for post-demodulation combining of RF downlink signals. The algorithms should be able to combine up to three streams of network data into a single seamless stream. The Taylor University team is to investigate the performance, feasibility, and value of this technology.
Results
RT Logic sent us 8 test sets in the form of PCAP network capture files. Each test set contains three lossy streams to be merged. We later received the original streams which can be used to calculate accuracy. The average results of the 8 test sets for each algorithm are shown below.
Interference
Merging Algorithm(s)
A | B |  | C
 | A | B | C
A | B | C
A | B | C
Problem
The three streams of data are produced when a satellite is in range of the ground stations and data transfer begins. Ideally, the three streams of data would be identical and contain no loss. However, packets do not always come in order and may be received with some error. Errors may include corruption, packet loss, out of sequence, and jitter. This means the algorithms should be able to account for these errors and pick the best combination of data from all three streams to produce a seamless stream that is as close to the original stream as is possible.
Objectives
Our team was given a list of requirements from RT Logic. We were tasked to create a system that had the ability to take in three streams of data in the form of a PCAP file and output a single, merged stream. The system was to have a command line interface for configuring the sources, output destination, algorithm, and other parameters. It also needed to provide statistics about algorithm execution time and quality of the merged stream. Each algorithm in the system should be able to handle the different forms of error and the data should be reconstructed as accurately as possible. Finally, we had the goal of being able to generate output data at 10 Mbps, with a configurable latency (that is, a longer latency between data arrival and stream production could allow for a better reconstruction.)
Testing Framework
We first decided to use Python for this project because of ease of use and the ability for us to get prototypes up and running quickly. We created a simple command line interface that takes in several parameters as inputs to test our developing algorithms. The framework parses the input streams and passes the parsed streams to the algorithm(s) to be processed. The framework has the ability to run the algorithms in parallel. After the algorithms have finished running, the framework displays statistics about the algorithm(s) and compares their performance and the quality of the merged stream for each algorithm.
Stream Generator
Another useful deliverable we worked on was an automated generator that generates a set of three corrupted input streams to feed into the algorithm(s). There are several parameters that can be configured to produce more or less erroneous streams. This is very useful in that it allows us to compare the output merged stream from the algorithm(s) to the original stream that was generated.
Algorithms
We developed three main algorithms. The first algorithm, called brute-force, has O(N3) complexity and so is quite slow. However, it is also accurate and looks for all possible combinations of data that can occur in at least two streams. Our second algorithm, multi-merge uses a similar strategy but it merges two streams together at a time. Our final algorithm, called hash, is our fastest algorithm and is also pretty accurate. It uses the Python dictionary to store all the combinations of the stream, then selects the data that occurs in at least two streams for final merged stream reconstruction.
Conclusion and Future Work
The hash algorithm has the most potential out of all of the algorithms with its fast execution time and good accuracy. Further research and algorithm development is needed but will be much easier with this testing framework in place.
Acknowledgements
Special thanks to Micah Russell for being our point of contact at RT Logic. Also special thanks Dr. White for guidance throughout the project.
Technologies Used
+Averages----------------+------------+-------+------------+ | | bruteForce | hash | multiMerge | +------------------------+------------+-------+------------+ | Accuracy (%) | 97.98 | 97.68 | 95.39 | | Block Size (B) | 100 | 100 | 100 | | Content Quality (%) | 98.11 | 99.22 | 98.98 | | Double Matches | 64 | 70 | 771 | | Execution Time (sec) | 69.121 | 0.181 | 168.511 | | Final Stream Size (B) | 76025 | 77150 | 77150 | | Processing Rate (Mb/s) | 0.24 | 5.585 | 0.266 | | Search Window Size (B) | 20000 | N/A | N/A | | Triple Matches | 695 | 701 | N/A | +------------------------+------------+-------+------------+ +Averages--------------------+----------+----------+----------+ | | Stream 1 | Stream 2 | Stream 3 | +----------------------------+----------+----------+----------+ | Length (B) | 74362 | 76175 | 76187 | | Similarity to Original (%) | 97.85 | 98.11 | 98.65 | +----------------------------+----------+----------+----------+
Department of Computer Science & Engineering, Taylor University,
Upland, Indiana, 46989